Insert an Infeed module:

Select Sinamics Integrated, insert new object, Infeed.

Name the object. Press continue.

Select the proper infeed module.

Check the settings both Voltage and frequency. Soft line conditions may require voltage to be set at 400V.

Choose the proper telegram for control.

Verify your settings. Press finish!

Open the configuration editor for Sinamics Intigrated. Press the Align with Hardware button.

If this module was not iinserted at the beginning of a project a warning message will be displayed.

Press “YES”. Simotion will then add the correct open addresses.

ADD CONTROL BLOCK. SEE OTHER SHEET.