Mapping Simotion D Inputs From Sinamics drive

The  Sinamics drives have built in I/O that can be utilised in your Simotion D project . You can also Map in TB30 I/O for use with your Simotion project .

Below is an example of adding the I/O to a Simotion D project from a Sinamics intergrated drive fitted with a TB30 I/O module .

- In the project hardware config , double click on the Sinamics integrated icon and select the configuration tab .

- Click on the activate button and select telegram 2 for slot 3 and 4

- Slot 3 is for the TB30 , and slot 4 is for the CU003 (Sinamics controller)

- Save and compile the hardware config

- In the Scout project screen , select the Sinamics_Integrated – configuration screen

- Click on the Align with HW Config button , and write down the I/O address ranges for the CU003 and the TB30 (you need these addresses later) .

- Now you need to assign the individual inputs of both the CU003 (integrated Sinamics controller) and the TB30 (expansion terminals) .

- To do the CU003 I/O first  , open the Sinamics Integrated – CU003 – Inputs/Outputs screen

- Now you need to map the Inputs across onto profibus as above .

- Now select the screen , Sinamics Integrated – CU003 – Communication – Profibus .

- You now need to set the profibus send and receive words up for the CU003 as below :-

- Now repeat the above procedure for the TB30 . First assigning the I/0 into a profibus word .

- Now set up the Profibus send and receive for the TB30 in the same manner as before :-

- At this point the inputs and outputs are mapped into the Profibus telegram to the Simotion D (Integrated profibus)

- You can now add these inputs and outputs to your Simotion D Project in the I/O config screen . Note at this point you need to know the profibus addresses from the hardware config earlier .

These inputs and outputs can now be used in the Simotion program as normal .